## Slide 1
Figure 2: System composition
Introduction
A data link is a system that transmits and processes tactical information in real time between sensors, command and control systems and weapon systems, with prescribed message format and communication protocols. The primary problem of data link system research and development is to design the system architecture according to user needs, and to clarify the relationship between the logical components.
MBSE and The Concept Model of The Internet of Things-Based Data Link System Designing Method
Peng Zhou, Fuqiang LI, Kai Zhang, Chubing Guo
Key Laboratory on Data Link, CETC
Method
In this paper, a complete system design process is proposed by drawing on the idea of model based systems engineering (MBSE) , and the design process of the data link system is standardized and unified. The system function is obtained by the requirement analysis. And the system composition structure is designed based on the conceptual model of the Internet of Things. In addition, the information interface relationship between the components of the system is described, which has strong guiding significance for the detailed design and development of the system in the next step.
Figure 1: Design flow
Summary
Compared with previous studies, this development method standardizes the analysis process and provides researchers with a clear and standardized design process. It makes the design process more intuitive and comprehensive, and is more conducive to the follow-up detailed design and research and development work. And it is also convenient for designers to trace and modify when requirements change, which helps to reduce workload and improve work efficiency.
Problems
There are generally three problems in the current research about designing the system architecture of data link. First, the existing data link system architecture is mostly proposed directly, which lacks a complete analysis under theoretical guidance. Second, the system design process is different, which is not unified and standardized. Third, there is a lack of research on the system composition structure, and lack of guidance for the detailed design of the system.
Results
This paper standardizes the design process of the data link system by the in-depth study of the design process of the data link system and the idea of MBSE. It is divided into three stages, i.e., requirements analysis, system architecture design and system composition structure design, as shown in Fig. 1.
In the requirements phase, the requirements are defined for data link users and the functional requirements are analyzed in detail. The system composition structure design is carried out with the help of the Internet of Things conceptual model. Finally, the composition of the data link system and the cross-linking relationship between each component are obtained, which provides a good foundation for the subsequent detailed design and development.
Based on the research and analysis in this paper, the entities in the system architecture are mapped to the Concept model of IoT. According to the actual needs to improve its content and cross-linking relationship, the composition structure and interface relationship of the data link system can be obtained, as shown in Fig. 2.
(3) The perception & control domain includes the entity set of the software and hardware systems that the data link system obtains the perception object information and manipulates the object, which mainly includes the information acquisition module and the control execution module. The perception & control domain realizes the localized perception, coordination and manipulation of the target object.
(4) The service provider domain is an entity collection of software and hardware systems that realizes the basic services and business services of the data link system. It can realize the processing and coordination of perception data, control data and service-related data, and provide users with situational awareness sharing, command and control guidance.
(5) The operation & maintenance management domain is a collection of entities, which includes the software and hardware systems that realize the operation and maintenance of the data link system and the supervision of compliance with specifications. It is used to monitor and manage the data link system to ensure its safe and reliable operation.
(6) The resource exchange domain includes an entity set of hardware and software systems that realize information sharing and exchange between data links.
And the associations between entities included in each domain are shown in Table 3 in the paper.
The descriptions of the entities contained in each domain in the composition structure of the data link system are as follows.
(1) The user domain includes a collection of software and hardware entities that realize the interaction between the data link user and the system, mainly the human-computer interaction interface.
(2) The target object domain includes a collection of perception and control objects of the data link system, including sensors, weapons, and avionics systems.