## Slide 1
Based on 2.5-D Large Angular Oblique Incidence and Polarization Insensitive Absorber Design
beibei ma1,*, xiaoxiang he2, yang yang3
（1beibei ma, Nanjing university of aeronautics and astronautics University, nanjing, China）
（2xiaoxiang he, Nanjing university of aeronautics and astronautics University, nanjing, China）
（3yang yang, Nanjing university of aeronautics and astronautics University, nanjing, China）
bbma0115@nuaa.edu.cn
This paper proposes a via-based novel metamaterial absorber (MA) for achieving stable energy absorption at/under oblique incidence of large angle. The TMVs of the absorber are located in the center of the patches to connect the two metal patches from different sides to achieve the miniaturization effect. This method reduces the center frequency of MA by introducing a vertical TMVs to play an important role in angle stability and p olarization insensitivity. A set of closed-form equations were applied to effectively calculate the circuit inductances and capacitances, and the changes caused by the addition of vias can be seen more visually. Meanwhile , according to the vector transmission line equations, the impedance characteristics of transmission line at large angular oblique incidence can be obtained, and the design of the absorber can be simplified by matching the impedance with that of the free space. Finally, a MA with angle stability and polarization insensitivity characteristic is designed. The simulation results show that when the oblique incident angle is in the range of 60 to 70 degrees, the bandwidth is 2GHz (from 11.98GHz to 13.11GHz) with a high absorptivity ( ≥9 0%) for both TE- and TM- mode.
INTRODUCTION
In this paper, we designed a MA for oblique incidence in the range of 50°~60° angle range using a 2.5-dimensional via structure. At the same time, the polarization stability of TE and TM is improved by adjusting the resistance in x and Y directions respectively, and the polarization stability of MA is improved. The simulation results show that the bandwidth of the MA is 2GHz (10.93GHz~13.03GHz) and the absorption can reach more than 90% in TE and TM polarization when the incident angle is between 50° and 60°. In this paper, the proposed structure based on 2.5-dimensional MAs is beneficial to the development of MAs at large Angle and oblique incidence.
CONCLUSION
RESULTS
METHODS
Fig.1.(a) Reflection coefficient of MA at TE polarization
Fig.2. (a)Reflection coefficient of MA at TM polarization
The absorptivity is characterized as follows:
A(ω)=1-R(ω)-T(ω) (1)
Where A( ω) is the absorptivity, R( ω) and T( ω) respectively are the reflection and transmission performance. In theory, because of the metallic ground plane and in order to maximize absorption, the any energy cannot transmit through the absorber, which means:
T(ω)=0 (2)
According to the expression to design for near-perfect absorber, it should satisfy that:
R( ω) = 0 (3)
R(ω)=1− (4)
Where S11 is reflection coefficient.